## Slide 1: Chapter 5 – Advection and Retardation

## Slide 2
Let’s take everything we have learned so far and now add in the two other processes discussed in the introduction chapter – advection and retardation

## Slide 3
Solve any way you want

## Slide 4: What does advection do?
Solve
Shifts the location of the peak

## Slide 5: What does retardation do?
Solve
Slows down time

## Slide 6: Can we still use a Greens function?
As long as our governing equation is linear, yes – you can always do it for a linear equation!
And – yes the ADE is linear. For the infinite domain the Greens function is given by

## Slide 7: Can we solve on a general domain?
What if our domain is not infinite (like in the problems in HW2)?
Well Polyanin’s book has an entire section with Greens functions for those problems too

## Slide 8: Can we use the same numerical methods?
Finite Differences
Random Walk

## Slide 9: Spatial Moments of a Plume
One of the features that is often used to characterize the nature of transport is the evolution of a plume’s spatial moments.
The nth moment of the plume is defined as
What does this represent?

## Slide 10: Centered Moments
It is usually useful to measure moments centered about the center of mass of the plume

## Slide 11: Moments
Zeroth (measures mass of system)
    Should be equal to 1 when normalized
First
    Tells you the location of the center of mass of the plume
Second
    Provides information about how wide the plume is (variance of the distribution)
Third
    Provides information on how skewed a plume is .

## Slide 12: So for ADE?

## Slide 13: Use these to classify models.
When second centered moment scales linearly in time
=> Fickian Dispersion
Anomalous/
Non-Fickian
Dispersion
Superdiffusion
Subdiffusion

## Slide 14: Sample Question
A geophysicist has provided you with the following plots of the first and second moment of a plume. Can you infer the advection speed and the dispersion coefficient?

## Slide 16: Temporal Moments of Breakthrough Curves
Another, less common, but increasingly popular method is to look at temporal moments of breakthrough curves (i.e. you have a concentration measurement at a fixed distance x and integrate over time)
It is often easier to measure breakthrough curves than spatial distribution of solutes and this information can also be used to infer parameters (such as v and D in the ADE).

## Slide 17: Evaluating these for ADE
For

## Slide 18: Example Problem
The following breakthrough curve is measured in a stream 100 meters downstream of a location where you injected a pulse of a conservative solute. The mass you threw in is 1 kg. The data associated with this curve in available for download. From this breakthrough curve can you infer the velocity of the water in the stream is and what the dispersion coefficient for the solute is?