## Slide 1: Flow to Wells

## Slide 2: Basic Assumptions
Aquifer bounded on the bottom
Horizontal Geologic Formations (with infinite extent)
The potentiometric surface is horizontal and is steady prior to pumping
Any changes in potentiometric surfaces are due to pumping
Aquifer is homogeneous and isotropic
All flow is radial towards the well
Groundwater flow is horizontal
Darcy’s Law is valid
Water has constant density and viscosity
Wells are fully penetrating
Pumping well has infinitesimal diameter and 100 efficiency

## Slide 3: Radial Flow
Two dimensional flow in a confined aquifer
Radial Transform
Axisymmetric
Radial Coords Flow Equations

## Slide 4: How about steady state conditions?
We will see how transient tests can be used to assess parameters, but steady state can provide a lot of information
Assumptions
  Pumping well is screened in aquifer being test only
  Observation wells are also screen in that aquifer only
  Both pumping and observation wells are screened throughout the entire aquifer thickness

## Slide 5: Steady State Confined Aquifer (Thiem solution)

## Slide 6: Steady State Confined Aquifer (Thiem solution)
Governing equation
Integrating between two wells at different radii

## Slide 7: Example Problem
Two observation wells are placed at a distance on 2 and 10 meters from a well.
The well is pumped at a flow rate of 800 litres/minute
The depth to water is 15m and 12 m for the first and second well respectively.
What is the transmissivity of the well.
If the depth of the aquifer is 10m, what is the hydraulic conductivity

## Slide 8: Steady State Unconfined Aquifer

## Slide 9: Steady State Unconfined Aquifer

## Slide 10: Steady State Unconfined Aquifer (Thiem solution)
Governing equation
Integrating between two wells at different radii

## Slide 11: Example Problem
Two observation wells are placed at a distance of 3 and 8 meters from a well in an unconfined aquifer
The well is pumped at a flow rate of 500 litres/minute
The depth to water is 5m and 2 m for the first and second well respectively.
If the depth of the aquifer is 10m, what is the hydraulic conductivity?

## Slide 12: Transients
Now we will consider transient (time-varying) solutions.
For some real situations it will simply take too long to reach steady state (equilibrium – let me hear it Brandon) conditions.
We can use transient analysis to infer aquifer properties, including storativity (which is not possible from steady measurements)

## Slide 13: Flow in a Completely Confined Aquifer – Theis’ Solution
Additional Assumptions
  Aquifer is confined on top and bottom
  No recharge
  Aquifer is compressible and water is released instantaneously
  Well is pumped at a constant rate

## Slide 14: Schematic Setup

## Slide 15: What does data typically look like?

## Slide 16: Governing Equations
Flow Equation
Initial Condition
Boundary Conditions

## Slide 17: Alternatively
Define drawdown
Flow Equation
Initial Condition
Boundary Conditions

## Slide 18: To Solve – Boltzman Transformation
Define
The flow equation and IC/BCs now become

## Slide 19: Solution
Let
Our equation becomes
Solution

## Slide 20: Solution
Solution
Recall
Therefore
This is called the exponential integral
and can be called from Matlab or any
good maths program

## Slide 21: Data from a pumping test
Known Q, known radius

## Slide 22
Approximately (for large times)
Using the graph on previous page (two unknowns – straight lines tells all)
Change in drawdown over one decade on log scale
Time when line intersects x axis

## Slide 23: Alternatively
We use the well function (tabulated in appendix 1 of the text by Fetter)

## Slide 24: Why use the tabulated function? Plot drawdown vs time in log log

## Slide 25: Overlay the Two and pick a match point (does not have to be on the curves – usually 1,1 on well function curve)
Using the match point, apply

## Slide 26: Example Problem (Matlab) Solve Both Ways
You are provided with the following pumping curve
The flowrate is 10m^3/s. The radius of the well is 10m
What is the transmissivity and storativity of the aquifer?

## Slide 27: What if the aquifer is leaky?
We include some form of flux from a confining layer
OR

## Slide 28: What if the aquifer is leaky?
Solution is given in terms of a tabulated function
where
W(u,r/B) is called the artesian well function and can be looked up
in Appendix 3 of Fetter

## Slide 29: What does the Artesian Well Function look like?

## Slide 30: Unconfined Aquifers
Assumptions
  Aquifer is unconfined
  Vadose zone has no influence on drawdown
  Water initially pumped comes from instantaneous release of water from elastic storage
  Eventually water from from storage due to gravity drainage
  Drawdown is negligible relative to saturated aquifer thickness
  The specific yield is at least 10 times the elastic storativity
  The aquifer can be anisotropic

## Slide 31: Unconfined Aquifers
Again, a tabulated results exists (water table aquifer pumping function - appendix 6)

## Slide 32: What does this pumping function look like?

## Slide 33
Graphical Methods with Match Point discussed in text book. They work just fine and I recommend that those of you who are interested read about them, but they are a little outdated with current computer capabilities.

## Slide 34: Slug Tests – The Poor Man’s Alternative
Pumping Tests are expensive for many many reasons (labor costs, well drilling costs, equipment, etc.). Sometime one way also not actually wish to extract water from an aquifer for fear that it may be contaminated.
Slug Tests (or their counterpart bail-down tests) are a cheap and quick alternative
A known quantity of water is quickly added or removed from a well and the response of water level in the well is measured.
Water does not have to be added – instead a slug of known volume can be thrown in, displacing a known volume of water.
Slug test responses can be overdamped or underdamped and different and appropriate methods must be chosen to properly analyse data.

## Slide 35: Overdamped Cooper-Bredehoeft-Papadopulos

## Slide 36: Overdamped Cooper-Bredehoeft-Papadopulos
We can show that (F is tabulated in appendix 2 of book)
Where
rc – radius of casing rs – radius of screen
Overlay data to identify what values of eta and mu correspond to your setup and
t1 is the time where on the type curve Tt/rc2=1

## Slide 37: Type Curves for Cooper-Bredehoeft-Papadopulos

## Slide 38: Sample Problem (Matlab)
Consider the following dataset and using the CBP method evaluate the Transmissivity and Storativity. Well and screen radius is 5 cm.
T(s) | H | H0 | H/H0
0.01 | 96.5 | 100 | 0.965
0.05 | 86 | 100 | 0.86
0.1 | 74.5 | 100 | 0.745
0.2 | 58 | 100 | 0.58
0.5 | 29 | 100 | 0.29
1 | 10.8 | 100 | 0.108
5 | 6.2 | 100 | 0.062
10 | 2.7 | 100 | 0.027
20 | 1.3 | 100 | 0.013

## Slide 39: Data from Example

## Slide 40: Overlay Graphics

## Slide 41: Overlay Graphics

## Slide 42: Overlay Graphics

## Slide 43: Overlay Graphics
Tt/rc2=1 on type curve plot

## Slide 44: Remove the Type Curve, but keep vertical line
When overlaid on Figure 5.19
We identify mu=1e-6 (see figure below)
t1=0.1
t1=0.1

## Slide 45: Overdamped Hvorslev Method

## Slide 46: Overdamped Hvorslev Method Interpretation
If the length of the piezometer is more than 8 times the radius of the well screen, i.e. Lc/R>8 then
K – hydraulic conductivity r – radius of the well casing R – radius of the well screen Le – length of the well screen t37 – time it take for the water level to rise or fall to 37% of the initial change.

## Slide 47: Example Problem
t(s) | H | H0 (cm) | H/H0
0.5 |  | 100 | 0.9
1 |  | 100 | 0.82
2 |  | 100 | 0.67
4 |  | 100 | 0.37
5 |  | 100 | 0.25
7 |  | 100 | 0.2
8 |  | 100 | 0.165
9 |  | 100 | 0.135
R=0.1m (radius of screen)
r=0.1m (radius of casing
L=5m (length of well screen)

## Slide 48: Data

## Slide 50: Overdamped Bouwer and Rice Method

## Slide 51: Overdamped Bouwer and Rice Interpretation
K – hydraulic conductivity rc – radius of the well casing R – radius of the gravel envelope Re – effective radius over which hear is disipated Le – length of screen over which water can enter H0 – drawdown at time 0 Ht – drawdown at time t t – time Lw – distance from water table to the bottom of the bore hole A,B – constants on figure 5.25
Valid for Lw<h (the saturated thickness of the aquifer)

## Slide 52: Underdamped Van der Kamp

## Slide 53: Underdamped Van der Kamp
Consider the following decay formula
Transmissivity given by
T – transmissivity rc – radius of well casing rs – radius of well screen S – storage coefficient L – effective length of the water column g – gravity w – angular frequency

## Slide 54: Steps in Van der Kamp
Calculate angular frequency w Dt – time between succesive peaks
Calculate damping factor
Solve implicit equation (iteratively)
Continue until converged

## Slide 55: Example Problem
Interpret the following curve
rc=0.5 m and rs=0.5m

## Slide 56: Cautions and Guidelines for Slug Tests
Skin Effects can yield underpredictions
Geological Survey Guidelines
  Three or more slug tests should be performed on a given well
  Two or more different initial displacement should be used
  The slug should be introduced as instantaneously as possible
  Good data acquisition equipment should be used
  An observation well should be employed for storage estimation
  Analysis method should be consistent with site
  Study results carefully and reassess analysis method if necessary
  Appropriate well construction parameters should be used

## Slide 57: Effects of Hydrogeologic Boundaries