## Slide 1: Properties of Aquifers

## Slide 2: Aquifer
An aquifer is a wet underground layer of water-bearing permeable rock or unconsolidated materials from which groundwater can be usefully extracted using a water well.

## Slide 3: Useful Definitions
Confining Layer – geologic unit with little or no intrinsic permeability
Aquifuge – Absolutely impermeable unit that will not transfer water
Aquitard – a layer of low permeability that can store ground water and transmit it slowly from one aquifer to another
Unconfined/Confined Aquifer – an aquifer without/with a confining layer on top.
Leaky Confined Aquifer – a confined aquifer with an aquitard as one of its boundaries
Perched Aquifer – a layer of saturated water that forms due to accumulation above an impermeable lens (e.g. clay)
Water Table – depth where the soil becomes completely saturated

## Slide 4: Topics
Aquifers are essentially porous media and so the properties relate to the properties of porous media:
Porosity
Grain Size Distribution
Specific Yield
Hydraulic Conductivity and Permeability
Compressibility

## Slide 5: Porosity
Porosity is the ratio of the volume of voids to the total volume
0<n<1, although sometimes we express it as a percentage by multiplying by 100
Question: How would you measure this?

## Slide 6: What does porosity depend on
Packing
Cubic Packing – Calculate the porosity….

## Slide 7: What does porosity depend on
Packing – what is we switch it up
VS.
Cubic vs Hexagonal vs Rhombohedral
(47.65%) (39.5%) (25.95%)

## Slide 8: Hexagonal Packing
Shift All Spheres on top layer one radius to the right

## Slide 9: Rhombohedral-Packed Spheres
Estimation of porosity accounting to this model:
Shift All Spheres on top layer one radius to the right and the shift forward one radius also

## Slide 10: Key Central Point
Porosity does not depend on the diameter of your grains!!!

## Slide 11: Heterogeneous Particle Sizes
Size and Shape of Grains makes a difference

## Slide 12: Example
Porous medium blended with three types of sediment fractions:
  Fine pebble gravel
  with porosity (pebble=0,30)
  Sand (sand=0,38)
  Fine sand (f.sand=0,33)

## Slide 13: Classification of Sediments
Engineering ASTM D2488 (Amer. Soc Testing Materials)

## Slide 14: Typical Porosity Ranges

## Slide 15: Grain Size Distribution
Very few materials have uniform grain sizes.
In order to measure the distribution of grains successively sieve materials through sieves of different size and build grain size distribution
Metrics – d10 and d60 (ten and sixty percentile diameters)
CU=d60/d10 – coeff of uniformity
CU<4 well sorted
CU>6 poorly sorted
d10 is called effective grain size

## Slide 16: Typical GSD
GSD of silty fine to medium sand – What is CU

## Slide 17: Typical GSD
GSD of fine sand – What is CU

## Slide 18: Specific Yield
Specific yield (Sy) is the ratio of the volume of water that drains from a saturated rock owing to the attraction of gravity to the total volume of the saturated aquifer.
Specific retention (Sr) is the rest of the water that is retained
Question: You have two materials with cubic packing; one is made up of small spheres, the other of larger ones; which has the larger specific retention? Think about the physics of what is retaining the water?

## Slide 19: Typical Specific Yields

## Slide 20: Hydraulic Conductivity
Henry Darcy – the father of groundwater hydrology

## Slide 21: Hydraulic Conductivity
Measure flowrate Q to estimate specific discharge (velocity)
q=Q/Area
Observations

## Slide 22: Darcy’s Law
Hydraulic Conductivity
Hydraulic Conductivity depends on both the
fluid and the porous medium

## Slide 23: Further Observations
In a bed of packed beads the flow rate is proportional to the diameter squared
The flow rate is proportional to the specific weight of the fluid
The flow rate is inversely proportional to the viscosity of the fluid

## Slide 24: Therefore
Property of the porous medium
only called intrinsic permeability
Denoted ki with units m2 (or Darcy’s)
1 Darcy=1x10-8cm2
Property of the fluid only
What drives the flow

## Slide 25: Typical Hydraulic Conductivities (for water)

## Slide 26: Hazen Formula for Hydraulic Conductivity
Recall from our classification of soils
Effective diameter d10
Hazen proposed that hydraulic conductivity is given by
K=C (d10)2
This is for water!!!!
C – shape factor (see adjacent table)
d10 in cm
K is given in cm/s
C shape factor
Very fine sand: C=40-80
Fine sand: C=40-80
Medium sand: C=80-120
Coarse sand: C=80-120 (poorly sorted)
Coarse sand: C=120-50 (well sorted, clean)

## Slide 27: How to Measure Permeability
Measure Volume V over time t
Hydraulic Conductivity is given by

## Slide 28: Falling Head Permeameter
Measure the drop in H over a time t

## Slide 29: Transmissivity
We like to think about groundwater in 2-dimensions (like a map).
Therefore we like to define the permeability over the depth of the aquifer (depth b)
Tranmissivity
T=bK

## Slide 30: Heterogeneity
Effective Hydraulic Conductivity – We like to replace heterogeneous blocks with analogous homogeneous ones
Replace with
Are they the same for the two – how would you do it?
K1
K2
VS.
K1
K2
Keff

## Slide 31: Heterogeneity
Effective Hydraulic Conductivity – We like to replace heterogeneous blocks with analogous homogeneous ones
K1
K2
K1
K2
Keff
Keff

## Slide 32: More Generally
N parallel layers, each with conductivity Ki of thickness bi
N perpendicular to flow layers, each with conductivity Ki of thickness bi
K1
K2
K3
KN
K1
K2
K3
K4

## Slide 33: Anisotropy
VS.
We therefore usually define a horizontal and vertical hydraulic conductivity
Kh and Kv
Coefficient of Anisotropy Kv/Kh - typically less than 1

## Slide 34: Formally
Darcy’s Law
where
q is a vector
K is a symmetric tensor (matrix) Kxy=Kyx
is a vector

## Slide 35: Sample Problem
You are provided with the following tensor for the hydraulic conductivity and the following hydraulic gradient. Determine the magnitude and direction of the resulting Darcy velocity. Units on the conductivity tensor are meters/second. Provide the final magnitude in meter per year.
dh/dx = 0.0013
dh/dy = -0.0021

## Slide 36: Hydraulic Gradient and Potentiometric Surface
3 well setup
Draw lines connecting wells
Note elevation at each well
Map distances between wells
Note difference in elevations
Find distance for unit head drop between wells
Mark even increments
Repeat for all well pairs
Create Contour Lines
Gradient normal to these lines

## Slide 37: Hydraulic Gradient and Potentiometric Surface
Right Angled Triangle