## Slide 1: Review Session 2 Flow to Wells

## Slide 2: Know at least a few of these Basic Assumptions (3-5)
Aquifer bounded on the bottom
Horizontal Geologic Formations (with infinite extent)
The potentiometric surface is horizontal and is steady prior to pumping
Any changes in potentiometric surfaces are due to pumping
Aquifer is homogeneous and isotropic
All flow is radial towards the well
Groundwater flow is horizontal
Darcy’s Law is valid
Water has constant density and viscosity
Wells are fully penetrating
Pumping well has infinitesimal diameter and 100 efficiency

## Slide 3: Steady State Confined Aquifer (Thiem solution)
Know how to translate depth to water information into head differences
i.e. h2-h1=d1-d2
Q is volume flow rate of well
r1 is radius from pumping well to observation well 1
r2 is radius from pumping well to observation well 2
h1 is head at well 1
h2 is head at well 2

## Slide 4: Steady State Unconfined Aquifer (Thiem solution)
Know how to translate depth to water (d) information into heads
b1= H-d1 b2=H-d2
You need to know depth of aquifer H
H
Q is volume flow rate of well
r1 is radius from pumping well to observation well 1
r2 is radius from pumping well to observation well 2
b1 is head at well 1
b2 is head at well 2

## Slide 5: Flow in a Completely Confined Aquifer – Theis’ Solution
Additional Assumptions (Again – know these)
  Aquifer is confined on top and bottom
  No recharge
  Aquifer is compressible and water is released instantaneously
  Well is pumped at a constant rate

## Slide 6: Data from a pumping test
Change in drawdown over one decade on log scale
Time when line intersects x axis
Q is volume flow rate of well
r1 is radius from pumping well to observation well 1

## Slide 7: Overlay the Two and pick a match point (does not have to be on the curves – usually 1,1 on well function curve)
Typically we pick match point such that W(u)=1 and u=1
Q is volume flow rate of well
r is radius from pumping well to observation well
h-h0 is drawdown on data at match point
t is time on data plot at the match point

## Slide 8: Slug Tests – The Poor Man’s Alternative
Pumping Tests are expensive for many many reasons (labor costs, well drilling costs, equipment, etc.). Sometime one way also not actually wish to extract water from an aquifer for fear that it may be contaminated.
Slug Tests (or their counterpart bail-down tests) are a cheap and quick alternative
A known quantity of water is quickly added or removed from a well and the response of water level in the well is measured.
Water does not have to be added – instead a slug of known volume can be thrown in, displacing a known volume of water.
Slug test responses can be overdamped or underdamped and different and appropriate methods must be chosen to properly analyse data.

## Slide 9: Overdamped Cooper-Bredehoeft-Papadopulos
rc is well casing radiius
rs is well screen radius
corresponds to best match curve (log10 mu=??)
t1 is the time on real data curve where on the type curve Tt/rc2=1 on best match type curve

## Slide 10: Overlay Graphics

## Slide 11: Overlay Graphics
Tt/rc2=1 on type curve plot

## Slide 12: Remove the Type Curve, but keep vertical line
When overlaid on Figure 5.19
We identify mu=1e-6 (see figure below)
t1=0.1
t1=0.1

## Slide 13: Overdamped Hvorslev Method
If the length of the piezometer is more than 8 times the radius of the well screen, i.e. Lc/R>8 then
K – hydraulic conductivity r – radius of the well casing R – radius of the well screen Le – length of the well screen t37 – time it take for the water level to rise or fall to 37% of the initial change.

## Slide 14: Overdamped Hvorslev Method Interpretation
If the length of the piezometer is more than 8 times the radius of the well screen, i.e. Lc/R>8 then
K – hydraulic conductivity r – radius of the well casing R – radius of the well screen Le – length of the well screen t37 – time it take for the water level to rise or fall to 37% of the initial change.

## Slide 16: Underdamped Van der Kamp
Then
Until converged

## Slide 17: Cautions and Guidelines for Slug Tests (Know these)
Skin Effects can yield underpredictions
Geological Survey Guidelines
  Three or more slug tests should be performed on a given well
  Two or more different initial displacement should be used
  The slug should be introduced as instantaneously as possible
  Good data acquisition equipment should be used
  An observation well should be employed for storage estimation
  Analysis method should be consistent with site
  Study results carefully and reassess analysis method if necessary
  Appropriate well construction parameters should be used