## Slide 1: Transport in Groundwater The Basics
Contaminant Transport

## Slide 2: In General
Recall the ADE in general is
If flow is incompressible
In GW we will consider transport in 2d in a uniform velocity field. Overhead view – because aquifers typically extend much further horizontally than they are deep.

## Slide 3: In General
The ADE in 2 d is
Question – why do I only consider velocity in x direction and not also in y?

## Slide 4: What is the advection velocity u?
Typically in groundwater systems we measure the Darcy velocity using Darcy’s law
Is velocity u just qx?
No – Darcy velocity is not the speed at which water actually moves, but a volume averaged velocity, which does not distinguish between fluid and solid phase in porous medium

## Slide 5: What is the advection velocity
Typically in groundwater systems we measure the Darcy velocity using Darcy’s law
ne – effective porosity
This is the actual average
Pore water velocity

## Slide 6: What about the Dispersion Term
As before dispersion causes ‘spreading’ of the solute plume
It is composed of two component
  molecular diffusion
  mechanical dispersion
  These can not be distinguished on the Darcy scale and so are lumped together

## Slide 7: Diffusion
Diffusion describes the spread of particles through random motion from regions of higher concentration to regions of lower concentration.
Fick’s Law - diffusive flux
The diffusion coefficient depends on the materials, temperature, electrical fields, etc.
Typically not as large as mechanical dispersion (but this is context specific)

## Slide 8: Mechanical Dispersion
Mechanical dispersion reflects the fact that not everything in the porous medium travels at the average water flow speed. Some paths are faster, some slower, some longer, some shorter. This results in a net spreading of the solute plume that looks very much like a diffusive behavior.
So are Dx and Dy (longitudinal and transverse) the same??

## Slide 9: Think about it on a medium like this.
Draw some particle trajectories
And then ask
Which is bigger?
Dmech,x or Dmech,y

## Slide 10: In Porous Media Mechanical Dispersion
Since mechanical dispersion depends on the flow, it can be shown that in the context of a a porous medium that it increase with increases flow speed. The exact relationship depends on many factor, but the most commonly applied model is the Scheidigger model, where The most common expression for mechanical dispersion is give by
a is called the dispersivity.
|u| is the absolute value of pore water velocity

## Slide 11: In Porous Media Mechanical Dispersion
a, the dispersivity, is different in the longitudinal and transverse directions.
Typically
What do you think that the dispersivity depends on? Look at its dimension when thinking about this.

## Slide 12: Retardation
When solutes flow through a porous medium they can interact with the solid phase. In particular they can sorb and desorb, which flows how quickly solutes moves relative the flowing water.
Recall conservation of mass
Split concentration into mobile and immobile concentrations
By definition j, the flux will only move Cm

## Slide 13: Mobile -Immobile
We can write a conservation equation that looks like this
Assume that mass transfers between mobile and immobile states faster than any other time scale in our system -> i.e. mobile and immobile concentrations balance immediately (equilibrium).
Equilibrium coefficient

## Slide 14: Mobile -Immobile
Combining everything we can write
Which we typically write as
Retardation coefficient

## Slide 15: What does retardation do
Slows down time
Or perhaps more intuitively – reduces transport rates
Effective velocities and dispersions are reduced by a factor R

## Slide 16: The Fundamental Solution
As before, in order to understand the role of each of these processes we will study how they affect a delta pulse initial condition
The delta function is like an infinitely thin
infinitely peaked pulse. It can be though of
as an approximation to a very narrow
exponential or Gaussian. An important property
is
This allows us to put in a desired mass

## Slide 17: Recall in 1-d
So, if you had to guess, what do you think the solution to this is

## Slide 18: Solution
Solution
Combine

## Slide 19: Movie

## Slide 20: What does this concentration distribution look like?
So what does this look like?
Let’s consider five cases and plot them at time t=10;
R=1; u=1; aL=0.1;x’=0;y’=0; Dmol=10-5;
R=2; u=1; aL=0.1;x’=0;y’=0; Dmol=10-5;
R=1; u=1; aL=1;x’=0;y’=0; Dmol=10-5;
R=1; u=10; aL=0.1;x’=0;y’=0; Dmol=10-5;
R=1; u=10; aL=1;x’=0;y’=0; Dmol=10-5;
Codes online

## Slide 21: Case 1
R=1; u=1; aL=0.1;x’=0;y’=0; Dmol=10-5;
What do you think the other cases will look like relative to this one?
R=2; u=1; aL=0.1;x’=0;y’=0; Dmol=10-5;

## Slide 22: Case 2
(ii) R=2; u=1; aL=0.1;x’=0;y’=0; Dmol=10-5;
(iii) R=1; u=1; aL=1;x’=0;y’=0; Dmol=10-5;

## Slide 23: Case 3
(iii) R=1; u=1; aL=1;x’=0;y’=0; Dmol=10-5;
(iv) R=1; u=10; aL=.1;x’=0;y’=0; Dmol=10-5;

## Slide 24: Case 4
(v) R=1; u=10; aL=1;x’=0;y’=0; Dmol=10-5;
(iv) R=1; u=10; aL=.1;x’=0;y’=0; Dmol=10-5;

## Slide 25: Case 5
(v) R=1; u=10; aL=1;x’=0;y’=0; Dmol=10-5;

## Slide 26: As before – Relevant Questions
How would we quantify the maximum concentration and how it evolves in time?
How do we quantify the position of plume?
How would we quantify the extent of the plume?

## Slide 27: As before – Relevant Questions
How would we quantify the maximum concentration and how it evolves in time?
How do we quantify the position of plume?
How would we quantify the extent of the plume?

## Slide 28: As before – Relevant Questions
How would we quantify the maximum concentration and how it evolves in time?
How do we quantify the position of plume?
How would we quantify the extent of the plume?

## Slide 29: As before – Relevant Questions
How would we quantify the maximum concentration and how it evolves in time?
How do we quantify the position of plume?
How would we quantify the extent of the plume?

## Slide 30: Different Mass Spill
M is the mass of the spill
Hopefully this
is obvious
to you

## Slide 31: Sample Problem
A spill of a contaminant into an aquifer has occurred. The spill was short and over a small area. The total mass of the spill is 10kg. You know from a recent study that the Darcy velocity of this aquifer is more or less uniform in one direction and of magnitude 2m/day. The effective porosity of the aquifer 0.3.
200m downstream of the spill location is a well field. There are five wells along a line perpendicular to the direction of flow located at y=-20,-10,0,10,20 (where y=0 aligns with the center of mass of the plume).
The molecular diffusion is 1e-9 m^2/s. The longitudinal dispersivity is 0.01 m.
Calculate concentration arriving at these well and plot breakthrough curves.
If you recall in one dimension – the area under these curves was a constant – is that the case here?

## Slide 32: Spatial Moments
Now moments consider x and y directions
Zeroth Moment m0,0
First Moments m1,0 and m0,1
Second Moment m2,0 and m0,2
Second Centered Moment (k11=m2,0-m21,0 , k22=m0,2-m20,1 )
What about the cross moments?? m1,1 and m2,2

## Slide 33: Moments
Zeroth Moment – 1 (normalized total mass)
First Moments – m1,0=ut and m0,1=0 (center of mass)
Second Moments – m2,0=2Dxt+u2t2 m0,2=2Dyt
Second Centered Moments k11=2Dxt k22=2Dxt
Note I have set R=1
Why?

## Slide 34: Sample Question
You have the following graphs for the longitudinal and transverse second centered moments. Can you from these graphs infer the ratio of longitudinal to transverse dispersivities.

## Slide 35: Question
We’ve been assuming that we can treat and aquifer as two dimensional.
When is it reasonable to do so?
You already know this from streams and rivers – so think about it.

## Slide 36: Degradation
What if we include first order degradation? Again – let’s set R=1 for simplicity.
What do you think the answer will be? Use everything you learned before to justify your answer

## Slide 37: Degradation
Again – just the conservative answer times exp(-gt)

## Slide 38: What about a different boundary condition/setup?
on x=0 between y=-L/2 and y=L/2
Answer is pretty huge – see next page…
Think about what this represents….

## Slide 39: Ridiculous Answer..
But what does it look like? – see Matlab script Steadystate.m
Can you tell if we
are neglecting anything
in this solution?

## Slide 40: Baseline parameter
In the Matlab script Steadystate.m we start with parameters
  u=0.01;
  alpha_L=1;
  alpha_T=alpha_L/10;
  C0=1;
  L=1;
  gamma=0.1;
  t=10;
Plot this solution and then vary them to see influence

## Slide 41: Steady State?
Consider steady state and a source
on x=0 between y=-L/2 and y=L/2
Doe this plume reach a steady state?

## Slide 42: Steady State
Do you see what happened? – Any estimate for how long it might take to reach steady state?

## Slide 43: Sample Problem
There is a continuous source of NAPL leaching toxins into an aquifer where the background flow is uniform with Darcy velocity 2m/day. The aquifer porosity is 0.25 and the longitudinal dispersivity is 0.01m.
The NAPL source aligns perpendicular to the flow and spans a width of 50 meters. Its concentration is 5g/liter.
In the absence of reaction how far down stream do you have to go along the plume centerline (where concentrations are highest) to get a concentration 104 times smaller than the source concentration.
By adding bacteria you can induce first order chemical reaction and the rate can be controlled based on the type and amount of bacteria you put in. If you need the distance where the concentration is 104 times smaller than the source concentration to be 1011 times smaller than what you calculated before, what reaction rate do you need to impose.